## Slide 1: Diffusion of Solar Photovoltaics and Role of Extremists
Jordi Fornt-Mas, Sourya Kovvali, Alejandro Nuñez-Jimenez, Marius Schwarz
Project for the lecture: Agent-Based Modeling and Social System Simulation, FS-2019, ETH Zurich December 9, 2019
Photo: EWZ

## Slide 2: Motivation
Cities account for three-quarters of human-caused global CO2 emissions
Cities account for two-thirds of global final energy use
REN21, 2019
Solar PV on the rooftop of buildings could generate 24% of Europe’s electricity demand
Bódis et al. 2019

## Slide 3: Motivation
Empirical studies show importance of active peer effects in solar communities
Noll et al. 2014
ABMs on opinion dynamics highlight the impact of extremism
Deffuant et al. 2002
Policies focus on energy communities to boost the diffusion of renewable energies
EU 2019/944
CH 2019 EnG, EnV
ABMs on solar PV diffusion focus on individual adoption or one-building communities
Schiera et al. 2019
Rai, Robinson 2015
What is the role of opinion extremists in the diffusion of individual and community solar photovoltaics in cities?

## Slide 4: Model and Agents

## Slide 5: Agent Profitability and Neighbourhood Pressure
Neighbor Factor
Fneighbor = ncommunity/ntotal
Profitability Factor
Fprofitability = 1 – PTi/PTmax
PTmax Maximum Payback time
PTi Payback time for agent i
PTi = IPV,i /CFPV,I
= price-per-watt . size
CFAC + CFFIR + CFOM
AC Avoided Costs
FIR Feed-in Remuneration
OM Operation and Maintenance Costs
Notes: Represented by the ratio of agents in the same block who have enrolled for community solar PV against total number of neighbors in the block
Defined by the payback period of the agent’s investment on installing and maintaining Solar PV

## Slide 6: Opinions and Interactions
Watts-Strogatz SWN
Clustering Coefficient 0.24
Average Shortest Path 3.65
Opinion and Uncertainty Model
Opinion of Agent i (Fopinion) xi
Uncertainty ui = xi (1 – xi)
Relative Agreement Algorithm
rai = max(0 , h/uj – 1)
xi’ = xi + μ rai (xi – xj)
ui’ = ui + μ rai (ui – uj)

## Slide 7: Tested Scenarios
One-Sided Extremism
+N% of Pos or Neg Extremists
Symmetric Extremism
+N% of Pos+Neg Extremists
Question: What is the role of opinion extremists in the diffusion of individual and community solar photovoltaics in cities?
20% N
5% N
Base
5% P
20% P
Experiments:
Base
5% (2.5%+2.5%)
10% (5%+5%)
20% (10%+10%)
40% (20%+20%)
Experiments:

## Slide 8: Results and Discussion

## Slide 9: Results and Discussion
One-Sided Extremism
Symmetric Extremism

## Slide 10: Results and Discussion
One-Sided Extremism
Symmetric Extremism

## Slide 11: Results and Discussion
RA
One-Sided
Extremism

## Slide 12: Results and Discussion
One-Sided
Extremism
Symmetric
Extremism

## Slide 13: Results and Discussion
One-Sided Extremism
Symmetric Extremism

## Slide 14: Results and Discussion
One-Sided Extremism
Symmetric Extremism

## Slide 15: Results and Discussion
Conclusions
“Single-Sided” extremism
  Unbalances average opinion towards that extreme
  However, average opinion of non-polarized nodes shifts to the opposite extreme

## Slide 16: Results and Discussion
Conclusions
“Single-Sided” extremism
  Unbalances average opinion towards that extreme
  However, average opinion of non-polarized nodes shifts to the opposite extreme
For Communities: Benefits of Pos. Extremists > Detriment by Neg. Extremists
  Neighbor Factor

## Slide 17: Results and Discussion
Conclusions
“Single-Sided” extremism
  Unbalances average opinion towards that extreme
  However, average opinion of non-polarized nodes shifts to the opposite extreme
For Communities: Benefits of Pos. Extremists > Detriment by Neg. Extremists
  Neighbor Factor
For Individual ideas: Relationship with Extremism is more complicated…
  Pos. Extremists  Install immediately and try to form communities
  But… Non-polarized nodes tend to compensate to the other extreme

## Slide 18: Questions and Answers

## Slide 19: What is the role of opinion extremists in the diffusion of individual and community solar photovoltaics in cities?
Jordi Fornt-Mas, Sourya Kovvali, Alejandro Nuñez-Jimenez, Marius Schwarz
Project for the lecture: Agent-Based Modeling and Social System Simulation, FS-2019, ETH Zurich December 9, 2019
Photo: EWZ

## Slide 20: What is the role of opinion extremists in the diffusion of individual and community solar photovoltaics in cities?
Jordi Fornt-Mas, Sourya Kovvali,
Alejandro Nuñez-Jimenez, Marius Schwarz
Project for the lecture: Agent-Based Modeling and Social System Simulation, FS-2019, ETH Zurich December 9, 2019
Photo: ESB Energy Service, Biel/Bienne